## Slide 1: Green Mars
Simon Rose & William Sellier
Deployable Greenhouse challenge.

## Slide 2: Objective
To develop an automated and self-deploying greenhouse on martian landscape as an advance life support system.

## Slide 3: Concept Diagram

## Slide 4: Basic Needs/Project Parameters
50 m2 growing area.
600 W*m-2 for photosynthesis.
Humidity:70%
Temperature:26.6°C
CO2 and O2 minimums.
Hypobaric conditions (28 kPa).

## Slide 5: Problems
600 W*m-2 is a lot of energy.
Heating the greenhouse.
Maintaining humidity.
Traditional growth media is heavy.

## Slide 6: Solutions!!!

## Slide 7: Aeroponics
http://www.microfarmsustainable.org/hydro.html

## Slide 8: Radiation Energy Required
Reduced from 600 W*m-2 to 260 W*m-2 by selecting only light wavelengths which are required for photosynthesis.

## Slide 9: Nuclear Power
Literature show small Advanced Stirling Radioisotope Generator capable of ~15 kW
NASA press release suggest small nuclear power units capable of up to 40 kW [They won’t talk to us about this… we tried].
This has added benefits…

## Slide 10: Temperature and Humidity
Using portion of waste heat for water vaporization and temperature control.
Forcing of air also provides minimum circulation required for plant growth.

## Slide 11: Closed Loop

## Slide 12: Estimated Specs
20 kW energy requirement.
24 kg of various gasses.
15 kg of water for aeroponic system.
~1600 kg total mass
9m diameter x 2.5m height
Not even a problem
for the Saturn V